## Slide 1: Lecture 7: TLB

## Slide 2: How to Run Multiple Processes
Time Sharing: one process uses RAM at a time
Static Relocation: statically rewrite code before run
Base: add a base to virtual address to get physical
Base+Bounds: also check physical addr is in range
Segmentation: many base+bounds pairs
Paging

## Slide 3: Page Mapping
VirtMem
PhysMem
P1
P2
P3
0 1 2 3 4 5 6 7 8 9 10 11
Page Tables
3
P1
1
7
10
0
P2
4
2
6
8
P3
5
9
11

## Slide 4: Addressing
For segmentation
  High bits => segment
  Low bits => offset
  Segment number vs. number of high bits
  Segment size vs. number of low bits
For paging
  High bits => page
  Low bits => offset
  Page number vs. number of high bits
  Page size vs. number of low bits

## Slide 5: Address Examples
How many low bits do we need, for page size 16 bytes, 1KB, 1MB, 512 bytes, and 4KB?
  4, 10, 20, 9, 12
How may page we can have for virtual address， with width 10, 20, 32, 16, and 32 bits correspondingly?
  64, 1K, 4K, 128, 1MB

## Slide 7: Translation Steps
H/W: for each mem reference:
1. extract VPN (virt page num) from VA (virt addr)
2. calculate addr of PTE (page table entry)
3. fetch PTE
4. extract PFN (page frame num)
5. build PA (phys addr)
6. fetch PA to register

## Slide 8: Memory Accesses with Paging
PT, load from 0x5000
Fetch instruction at 0x2010
PT, load from 0x5004
Exec, load from 0x0100
…
0x0010 movl 0x1100, %r8d
0x0014 addl $0x3, %r8d
0x0017 movl %r8d, 0x1100
2
PT
0
80
99
Assume PT is at 0x5000
Assume PTE’s are 4 bytes
Assume 4KB pages

## Slide 9: Other Information in Page Table
What other data should go in page table entries besides translation?
  valid bit
  protection bits
  present bit
  reference bit
  dirty bit

## Slide 10
offset = VirtualAddress & OFFSET_MASK
PhysAddr = (PFN << SHIFT) | offset
1 // Extract the VPN from the virtual address
2 VPN = (VirtualAddress & VPN_MASK) >> SHIFT
3
4 // Form the address of the page-table entry (PTE)
5 PTEAddr = PTBR + (VPN * sizeof(PTE))
6
7 // Fetch the PTE
8 PTE = AccessMemory(PTEAddr)
9
10 // Check if process can access the page
11 if (PTE.Valid == False)
12 RaiseException(SEGMENTATION_FAULT)
13 else if (CanAccess(PTE.ProtectBits) == False)
14 RaiseException(PROTECTION_FAULT)
15 else
16 // Access is OK: form physical address and fetch it
17 offset = VirtualAddress & OFFSET_MASK
18 PhysAddr = (PTE.PFN << PFN_SHIFT) | offset
19 Register = AccessMemory(PhysAddr)

## Slide 11: Memory Accesses Again
PT, load from 0x5000
Fetch instruction at 0x2010
PT, load from 0x5004
Exec, load from 0x0100
…
0x0010 movl 0x1100, %r8d
0x0014 addl $0x3, %r8d
0x0017 movl %r8d, 0x1100
2
PT
0
80
99
Assume PT is at 0x5000
Assume PTE’s are 4 bytes
Assume 4KB pages
TOO SLOW

## Slide 12: A Memory Trace
int array[1000];
...
for (i = 0; i < 1000; i++)
array[i] = 0;
0x1024 movl $0x0,(%edi,%eax,4)
0x1028 incl %eax
0x102c cmpl $0x03e8,%eax
0x1030 jne 0x1024

## Slide 14: TLB: Basic strategy
Take advantage of repetition.
Use a CPU cache.
CPU
TLB
RAM
PT
Notes: ATC?

## Slide 15: TLB Cache Type
Fully-Associative: entries can go anywhere
  most common for TLBs
  must store whole key/value in cache
  search all in parallel
There are other general cache types

## Slide 16: TLB Contents
VPN | PFN | other bits
TLB valid bit
  whether the entry has a valid translation
TLB protection bits
  rwx
Address Space Identifier
TLB dirty bit

## Slide 17
1 VPN = (VirtualAddress & VPN_MASK) >> SHIFT
2 (Success, TlbEntry) = TLB_Lookup(VPN)
3 if (Success == True) // TLB Hit
4 if (CanAccess(TlbEntry.ProtectBits) == True)
5 Offset = VirtualAddress & OFFSET_MASK
6 PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
7 AccessMemory(PhysAddr)
8 else
9 RaiseException(PROTECTION_FAULT)
10 else // TLB Miss
11 PTEAddr = PTBR + (VPN * sizeof(PTE))
12 PTE = AccessMemory(PTEAddr)
13 if (PTE.Valid == False)
14 RaiseException(SEGMENTATION_FAULT)
15 else if (CanAccess(PTE.ProtectBits) == False)
16 RaiseException(PROTECTION_FAULT)
17 else
18 TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
19 RetryInstruction()

## Slide 18: Reasoning about TLB
Workload: series of loads/stores to accesses
Metric: performance (i.e., hit rate)

## Slide 19: Array Iterator with TLB
int sum = 0;
for (i = 0; i < 10; i++) {
sum += a[i];
}
How many TLB hits?
How many TLB misses?
Hit rate?
Miss rate?
Notes: TLB
Valid VPN PFN
0
0
0
0
What’s the virtual address for a[0]
0x604, and the following?
PTBR+24, 0xA04
PTBR+24, 0xA08
PTBR+24, 0xA12

## Slide 20: TLB Workloads
Spatial locality
  Sequential array accesses can almost always hit in the TLB, and so are very fast!
Temporal locality
What pattern would be slow?
  highly random, with no repeat accesses

## Slide 21: Who Handles The TLB Miss?
H/W or OS?
H/W: CPU must know where page tables are
  CR3 on x86
  Page table structure not flexible
OS: CPU traps into OS upon TLB miss

## Slide 22
1 VPN = (VirtualAddress & VPN_MASK) >> SHIFT
2 (Success, TlbEntry) = TLB_Lookup(VPN)
3 if (Success == True) // TLB Hit
4 if (CanAccess(TlbEntry.ProtectBits) == True)
5 Offset = VirtualAddress & OFFSET_MASK
6 PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
7 AccessMemory(PhysAddr)
8 else
9 RaiseException(PROTECTION_FAULT)
10 else // TLB Miss
11 PTEAddr = PTBR + (VPN * sizeof(PTE))
12 PTE = AccessMemory(PTEAddr)
13 if (PTE.Valid == False)
14 RaiseException(SEGMENTATION_FAULT)
15 else if (CanAccess(PTE.ProtectBits) == False)
16 RaiseException(PROTECTION_FAULT)
17 else
18 TLB_Insert(VPN, PTE.PFN, PTE.ProtectBits)
19 RetryInstruction()

## Slide 23
1 VPN = (VirtualAddress & VPN_MASK) >> SHIFT
2 (Success, TlbEntry) = TLB_Lookup(VPN)
3 if (Success == True) // TLB Hit
4 if (CanAccess(TlbEntry.ProtectBits) == True)
5 Offset = VirtualAddress & OFFSET_MASK
6 PhysAddr = (TlbEntry.PFN << SHIFT) | Offset
7 AccessMemory(PhysAddr)
8 else
9 RaiseException(PROTECTION_FAULT)
10 else // TLB Miss
11 RaiseException(TLB_MISS)

## Slide 24: OS TLB Miss Handler
OS: CPU traps into OS upon TLB miss
  check page table for page table entry
  if valid, extract PFN and update TLB w a special inst
  return from trap
Where to resume execution?
  The instruction that caused the trap
How to avoid double traps?
  keep TLB miss handlers in physical memory
  reserve some entries in the TLB for permanently-valid translations
Modifying TLB entries is privileged

## Slide 25: TLB Contents
VPN | PFN | other bits
TLB valid bit
  whether the entry has a valid translation
  Different from page table valid bit
TLB protection bits
  rwx
Address Space Identifier
TLB dirty bit