## Slide 1: Lecture 16 I/O Devices & Hard Disk Drives

## Slide 2: We need I/O devices

## Slide 3: The Canonical Device
  Micro-controller (CPU)
  Memory (DRAM or SRAM or both)
  Other Hardware-specific Chips
Status
Command
Data
Device Registers
Hidden Internals
The interface for OS to interact

## Slide 4: The Canonical Protocol
While (STATUS == BUSY) // 1
; // wait until device is not busy
Write data to DATA register // 2
Write command to COMMAND register // 3
(To start the device & executes the command)
While (STATUS == BUSY) // 4
; // wait until device is done with your request

## Slide 5: A trace
CPU:
Disk:
A
B
C
A
3
1 2 4

## Slide 6: Using interrupts to avoid spinning
CPU:
Disk:
A A A
B
C
A
1 3,4
2
B
B

## Slide 7: Interrupts vs. Polling
Discussion: could interrupt be worse under some cases?
Techniques:
  Hybrid approach
  Interrupt coalescing

## Slide 8: What else can we optimize?
CPU:
Disk:
A A A
B
C
A
1 3,4
2
B
B

## Slide 9: Programmed I/O vs. Direct Memory Access
PIO (Programmed I/O):
  CPU directly tells device what data is
DMA (Direct Memory Access):
  CPU leaves data in memory
  Device reads it directly

## Slide 10: Using DMA
CPU:
Disk:
A A
B
C
A
1 3,4
B
B

## Slide 11: How does OS access registers?
Special instructions
  each device has a port
  in/out instructions (x86) communicate with device
Memory-Mapped I/O
  H/W maps registers into address space
  loads/stores sent to device
Doesn’t matter much (both are used).

## Slide 12: Protocol Variants
Status checks: polling vs. interrupts
Data: PIO vs. DMA
Control: special instructions vs. memory-mapped I/O

## Slide 13: Variety is a Challenge
Problem:
  many, many devices
  each has its own protocol
How can we avoid writing a slightly different OS for each H/W combination?
  Encapsulation!
  Write driver for each device.
  Drivers are 70% of Linux source code.

## Slide 14: The File System Stack

## Slide 15: Hard Disk Basic Interface
Disk has a sector-addressable address space (so a disk is like an array of sectors).
Sectors are typically 512 bytes or 4096 bytes.
  By the end of 2007, Samsung and Toshiba began shipments of 1.8-inch hard disk drives with 4096 byte sectors. In 2010, the International Disk Drive Equipment and Materials Association (IDEMA) completed the Advanced Format standard for 4096 sector drives, setting the date for the transition from 512 to 4096 byte sectors as January 2011 for all manufacturers, and Advanced Format drives soon became prevalent. [wiki]
Main operations: reads + writes to sectors.

## Slide 16: Disk Internals
Platter: covered with a magnetic film.
Surface: each platter has two surfaces
Spindle: many platters may be bound to the spindle.
Track: each surface is divided into rings, each track is further divided into numbers sectors
Cylinder: a stack of tracks across platters
Heads on a moving arm can read from each surface.

## Slide 17: Three Tracks Plus A Head

## Slide 18
https://www.youtube.com/watch?v=9eMWG3fwiEU

## Slide 19: Seek, Rotate, Transfer
Must accelerate, coast, decelerate, settle
Seeks often take several milliseconds!
Settling alone can take 0.5 - 2 ms.
Entire seek often takes 4 - 10 ms.

## Slide 20: Seek, Rotate, Transfer
Depends on rotations per minute (RPM).
  7200 RPM is common, 15000 RPM is high end.
1 / 7200 RPM = 1 minute / 7200 rotations = 1 second / 120 rotations = 8.3 ms / rotation
so it may take 4.2 ms on avg to rotate to target (0.5 * 8.3 ms)

## Slide 21: Seek, Rotate, Transfer
Pretty fast — depends on RPM and sector density.
100+ MB/s is typical.
1s / 100 MB = 10 ms / MB = 4.9 us / sector (assuming 512-byte sector)

## Slide 22: Workload
So…
  seeks are slow
  rotations are slow
  transfers are fast
What kind of workload is fastest for disks?
  Sequential: access sectors in order (transfer dominated)
  Random: access sectors arbitrarily (seek+rotation dominated)

## Slide 23: Disk Spec
Sequential workload: what is throughput for each?
  Close to max transfer rate if workload large enough
Random workload: what is throughput for each?
  Assume 4KB reads: 0.66MB/s and 0.31MB/s
  Assume 16KB reads: 2.5 MB/s and 1.2MB/s
Notes: avg rotation =1/2 x 1 min/15000 x 60 sec/1 min x 1000 ms/1 sec= 2 ms
transfer =1 sec/125 MB x 16 KB x 1,000,000 us/1 sec= 125 us
Cheetah time = 4ms + 2ms + 125us = 6.1ms
throughput =16 KB/6.1ms x 1 MB/1024 KB x 100 ms/1 sec =2.5 MB/s
avg rotation =1/2 x 1 min/7200 x 60 sec/1 min x 1000 ms/1 sec= 4.1 ms
transfer =1 sec/105 MB x 16 KB x 1,000,000 us/1 sec= 149 us
Cheetah time = 9ms + 4.1ms + 149us = 13.2ms
throughput =16 KB/13.2ms x 1 MB/1024 KB x 100 ms/1 sec =1.2 MB/s

## Slide 24: Track Skew

## Slide 25: Zones

## Slide 26: Other Improvements
Track Skew
Zones
Cache
  Drives may cache both reads and writes.

## Slide 27: Schedulers
Given a stream of requests, in what order should they be served?
FCFS
Try to follow SJF (shortest job first)
SSTF: Shortest Seek Time First
  Difficult for OS, OS can do nearest-block-first (NBF)
  Starvation
Elevator (a.k.a. SCAN or C-SCAN)
  Still ignore rotation time

## Slide 28: SPTF: Shortest Positioning Time First

## Slide 29: Other Issues
Both OS and disk do some scheduling
I/O merging
Work Conservation

## Slide 30: Next: File System Implementation

## Slide 31: The File System Stack

## Slide 32: File and File Name
What is a File?
  Array of bytes.
  Ranges of bytes can be read/written.
File system consists of many files, and files need names so programs can choose the right one.
  inode
  path
  file descriptor

## Slide 33: inodes
Each file has exactly one inode number.
inodes are unique (at a given time) within a FS.
Different file system may use the same number, numbers may be recycled after deletes
Show inodes via stat.

## Slide 34: Paths
String names are friendlier than number names.
Store path-to-inode mapping in many files. Call these special files directories.
Reads for getting final inode called “traversal”.

## Slide 35: File Descriptor (fd)
Idea: do traversal once, and store inode number in descriptor object. Do reads/writes via descriptor. Also remember offset.
A file-descriptor table contains pointers to file descriptors.
The integers you’re used to using for file I/O are indexes into this table.

## Slide 36: Code Snippet
int fd1 = open(“file.txt”); // returns 3
read(fd1, buf, 12);
int fd2 = open(“file.txt”); // returns 4
int fd3 = dup(fd2); // returns 5
offset = 0
inode =
offset = 0
inode =
location = 0
size =
inode
fds
fd table
0
1
2
3
4
5
offset = 12
inode =